## Slide 1
Presented by
Vasanth P, Vishal G, Sibi V B, Yuvasaravanan S
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)
Vasanth P, Vishal G, Sibi V B, Yuvasaravanan S - M.Kumarasamy College of Engineering, Department of Electronics and Communication Engineering
Paper ID-ECE137
Approximate vedic multiplier using low order compressors

## Slide 2
Introduction
Previous Works
Proposed Scheme
Experimental Details
Results and Analysis
Conclusions
Introduction
1/7
Now a days as the digital units are becoming hand held and portable there is a great need for systems that consume less power.
By minimizing the power consumption and area utilization of the units of the system we can minimize the overall power consumption.
Approximate arithmetic techniques are applied at circuit level or algorithm level to minimize the power dissipation and area utilization of the system
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 3
Introduction
Previous Works
Proposed Scheme
Experimental Details
Results and Analysis
Conclusions
Previous Works
2/7
The compressors are used to design the high speed multipliers, to minimize the delay in the summation part of the partial product.
The 4-2 compressor is implemented using XOR-XNOR gates and 2:1 multiplexers. This 4-2 compressor has five inputs in which one carry input and two outputs.
The 3-2 compressor has three inputs and two outputs, it is similar to FA(full adder).
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 4
Introduction
Related Works
Proposed Scheme
Experimental Details
Results and Analysis
Conclusions
Proposed Scheme
3/7
This is implemented and used by Indian mathematicians.
The 4 × 4 multiplier is designed based on the Vedic mathematics using proposed compressor, in first stage bitwise logical AND operation is performed .
In the first stage, sixteen logical AND gates are used from least significant Bit(LSB) to most significant bit(MSB) to compute single bit output.
The main aim of replacing all general compressors with approximate compressors is to minimize the delay, power and area significantly.
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 5
Introduction
Related Works
Proposed Approach
Experimental Details
Results and Analysis
Conclusions
Experimental Details
4/7
Modified full adder
One carry save adder
Fast adders
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 6
Introduction
Related Works
Proposed Approach
Experimental Details
Results and Analysis
Conclusions
Results and Analysis
5/7
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 7
Introduction
Related Works
Proposed Approach
Experimental Details
Results and Analysis
Conclusions
Conclusions
6/7
This work has shown that multiplier can be used for approximate computing by an approximate design of a compressor; this proposed multiplier gives better results in terms of design parameters compared to existing multipliers, and in terms of accuracy metrics, critical path delay, area and power.
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 8
Introduction
Related Works
Proposed Approach
Experimental Details
Results and Analysis
Conclusions
References
7/7
[1].J. Han and M. Orshansky, "Approximate computing: An emerging paradigm for energy-efficient design", 18th IEEE European Test Symposium (ETS), 2013.
[2].V. Gupta, D. Mohapatra, A. Raghunathan, and K. Roy, “Low-power digital signal processing using approximate adders,” IEEE Trans. Comput.-Aided Design Integr. Circuits Syst., vol. 32, no. 1, pp. 124–137,Jan. 2013.
[3] E. J. King and E. E. Swartzlander, Jr., “Data-dependent truncation scheme for parallel multipliers,” in Proc. 31st Asilomar Conf. Signals,Circuits Syst., Nov. 1998, pp. 1178–1182.
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)

## Slide 9
?
Q and A?
IETE sponsored National Conference on Innovative Research in Electrical,
Electronics and Communication Engineering (ELECTROX’23)